## Slide 1: Scheduling
Chapter 6
Notes: during the past two decandes many industrial companies changed their inventory systems -> from reorder point systems (independent-demand system) to MRP systems (dependend-demand systems). approach was developed in early 70s
appropriate for considering complex products, assembled of various components and subassemblies
major objective: determine requirements (discrete demand for each component in each time bucket) -> used to generate infomration required for correct material purchasing or shop-floor production

## Slide 2: Production Planning & Control (PPC)
Produktionsplanung & Steuering (PPS)
Production planning
  MPS
  MRP
  Lotsizing
  Capacity checks…
Production control
  Job release
  Scheduling

## Slide 3: Job Release
Flow time = completion time – release time
If jobs are released too early (e.g. based on historical data on flow times + some safety times)
Long queues before machines (esp. bottlenecks)
Long observed flow times
Jobs are released even earlier
Even longer queues before machines
Even longer observed flow times
Etc. … vicious circle

## Slide 4: Job release
To break this vicious circle  systematic job release
Basic idea: „release job only when the utimization of the sysstem is below a certain threshold“
2 simple strategies:
  CONWIP = CONstant Work In Process simple, used in US literature „keep „work in process“ (WIP) constant, i.e. release a new job eas soon assome job is finished
  „belastungsorientierte Auftragsfreigabe“ (BOA, BORA) („utilitazion based job release“) more complicated measure for utilization of the system mainly German literature

## Slide 5: Scheduling
After job release there are queues of jobs in front of the various machiens
Decide in which order these are processed (and also the starting times)  scheduling
Various objectives are reasonable, e.g.
      Minimize total tardiness,
      Minimize cycle time (max completion time) Z
      Minimize average (or total) flow time D.
 Unfortunately most objectives are conflicting!

## Slide 6: Single Machine Scheduling
Scheduling is typically np-hard
Single machine scheduling is relatively easy
Many problems can be solved to optimality (exact algorithm) using some simple priority rules (list scheduling)
Examples:
Minimize maximum tardiness
Minimize cycle time Z
Minimize average flow time D

## Slide 7: Tardiness
QEM- Mgmt Sci
Chapter 6/7
Given: due date (desired completion time)
Observed after scheduling: actual completion time
Lateness = completion time - due date
Can be positive or negative
  If lateness > 0 … job is late Tardiness = max {0, lateness}
  If lateness < 0 … job is early Earliness = max {0, - lateness}
Simple rule good for all tardiness related objectives:
Earliest Due Date (EDD) rule

## Slide 8: Minimize Maximum Tardiness
EDD rule, always schedule job with earliest due date first
Is an exact algorithm for maximum tardiness
Example:
job | processing time | due date | rank | Completion time | tardiness
A | 6 | 8 |  |  | 
B | 2 | 6 |  |  | 
C | 8 | 18 |  |  | 
D | 3 | 15 |  |  | 
E | 7 | 21 |  |  | 
1.
4.
5.
3.
2.
8
2
11
19
26
-
-
-
1
5
Optimal sequence:
B  A  D  C  E
Completion times? Tardiness?  Gantt chart
QEM- Mgmt Sci
Chapter 6/8
overview

## Slide 9: EDD Example – Gantt Chart
A
E
C
D
B
8
11
19
26
V = maximum tardiness =
T = total tardiness =
5
5+1
= 6
2
21
18
15
8
6
cycle time
D = average flow time =
(8+2+19+11+26)/5
= 13,2
#T = number of tardy jobs
= 2

## Slide 10: Other Objectives Related to Tardiness
Minimize sum of all tardinesses (total tardiness) in above example: total tardiness = 1 + 5 = 6 typically np-hard (at least if objective is weighted) EDD rule is a good heuristic
Minimize number of tardy jobs in above example: number of tardy jobs = 2
Can be solved to optimality with Hodgson‘s algorithm:
Apply EDD rule
If a job is late  remove scheduled task with the longest operation time
All removed task are schedules last and will be tardy
All scheduled (and not removed) tasks will be on time

## Slide 11: Minimize Cycle Time Z
Cycle Time (makespan) = maximum completion time of all jobs
„Minimize Cycle Time“ is typically conflicting with all other objectives
Single machine scheduling: problem is trivial: every schedule without idle times is optimal
Above Example: Z is always 26, unless idle times are scheduled

## Slide 12: Minimize Average Flow Time
Optimal Solution: SPT rule (shortest processing time)
job | processing time | rank | due date | completion time | tardiness
A | 6 |  | 8 |  | 
B | 2 |  | 6 |  | 
C | 8 |  | 18 |  | 
D | 3 |  | 15 |  | 
E | 7 |  | 21 |  | 
3.
1.
5.
2.
4.
26
18
5
2
11
3
-
8
-
-
Optimal sequence:
B  D  A  E  C
QEM
Chapter 6/12
overview
Completion times? Tardiness?  Gantt chart

## Slide 13: SPT Example – Gantt Chart
B
D
A
E
C
2
5
11
18
26
V = maximum tardiness =
8
( > 5 with EDD)
D = average flow time =
(11+2+26+5+18)/5
= 12,4
( < 13,2)
max tardiness and average flow time are conflicting

## Slide 14: Scheduling With Multiple Machines
Main classes of problems:
Flow shop … same sequence of machines for all jobs (but sequence of jobs at machines can be different – to be optimized)
Permutation Flow shop … no overtaking is possible (same sequence of jobs at all machines – to be optimized)
Job shop … each job can have a different required sequence of machines
Open shop … required sequence of machines is free

## Slide 15: Scheduling With Multiple Machines
Each job must be processed on several machines
Typically np-hard  heuristic solution
SPT: shortest (total) processing time good for average flow time (optimal for single machine)
SOT: shortest operation time good for average flow time (optimal for single machine)
SRPT: shortest remaining processing time total processing time on remaining machines often best for average flow time
LPT, LOT: longest processing/operation time sometimes good for cycle time Z
EDD: (earliest due date) – all due date related objectives
Critical ratio: clever variant of EDD rule (remaining time to due date)/(remaining processing time)

## Slide 16: Scheduling With Two Machines
2 machines
flow shop (same sequence of machines for all jobs)
Objective “minimize cycle time”
 Optimal solution is a permutation schedule:
Johnson Algorithm:
1. Find smallest element in table of operation times. If this occurs with machine 1, schedule on first available position, otherwise schedule on last available position.
2. Delete schedules jobs from list of open jobs
Example

## Slide 17: Example - Johnson Algorithm
Given: 5 jobs ans 2 machines M1 and M2
Minimize cycle time!
job | M1 | M2 | Flow time (Johnson) | Total (remaining) processing time | Flow time (SRPT)
A | 5 | 2 |  |  | 
B | 3 | 6 |  |  | 
C | 8 | 4 |  |  | 
D | 10 | 7 |  |  | 
E | 7 | 12 |  |  | 
Optimal sequence:
[     ]
2
3
4
7
B
C
E
D
A
7
17
9
12
19
35
9
33
29
22
7
14
20
33
45
flow times, cycle time?
EK Produktion & Logistik
Kapitel 10/17

## Slide 18: Example – Gantt Chart
B
E
D
C
A
B
E
C
A
3
28
20
10
35
33
29
22
10
9
3
33
Z = cycle time =
D = average flow time =
(9+22+29+33+35)/5
= 25,6
35 ZE
D
Job B can start on machine M2, as soon as finished on M1 (M2 idle)
Job E can start on machine M2, as soon as finished on M1 (M2 idle)
Job D cannot start on M2 as soon as finished on M1 fertig (M2 occupied)

## Slide 19: Example – SRPT Rule
Apply SRPT rule ( try to get a shorter average flow time)
sequence: [     ]
A
B
C
D
E
A
B
E
C
D
A
B
C
D
5
8
16
26
33
14
20
26
33
45
5
7
8
16
Z = cycle time =
D =
45 ZE
(7+14+20+33+45)/5 =
23,8
( > 35 Johnson)
( < 25,6 Johnson)
E